## Slide 1
Doug N. Blewitt
Certified Consulting Meteorologist
Air Quality Resource Management (AQRM)
September 15, 2021
WEG Comments on Oil and Gas Ozone Impacts

## Slide 2: WEG Comments on Oil and Gas Ozone Impacts
From WEG comment on oil and gas contribution to New Mexico ozone formation
“To begin with, it is important to highlight the longstanding understanding that the oil and gas industry’s ozone precursor emissions can have significant impacts on regional ozone formation and cause or contribute to exceedances and even violation of the NAAQS, particularly in the western United States. Studies and firsthand experience have confirmed the myriad sources of VOC and NOx emissions associated with oil and gas extraction can produce large amounts of ozone-forming pollution and contribute to exceedances and/or violations of the NAAQS.”

## Slide 3: WEG Comments on Oil and Gas Ozone Impacts (continued)
There are two specific and unique instances where oil and gas emissions resulted in a measured exceedance of the ozone NAAQS, Uinta Basin in Utah and the Greater Green Basin in Wyoming
In both cases the exceedances occurred during the winter season under specific and unique meteorological conditions:
Fresh snow cover
A very low inversion that capped emissions within the boundary layer
Strong solar radiation
Terrain that formed a slight bowl that further inhibited advection of pollutants and
Very stable atmospheric conditions
Under these conditions, emissions were trapped within a confined area and the low inversion reduced vertical mixing. Emissions were concentrated within a confined volume and when exposed to high solar radiation, photochemical reactions occurred and resulted in the formation of elevated ozone concentrations
Conclusion
There is no specific data to suggest that the unique meteorological conditions that resulted in winter ozone exceedances in Utah and Wyoming will occur in New Mexico