## Slide 1: Commercial Disposal Group: Definition Storage Vessels, Section 7.RR
Proposed Language
20.2.50.7.RR. Definitions:
RR. “Storage vessel” means a single tank or other vessel that is designed to contain an accumulation of hydrocarbon liquid or produced water and is constructed primarily of non earthen material including wood, concrete, steel, fiberglass, or plastic, which provide structural support. A well completion vessel that receives recovered liquid from a well after commencement of operation for a period that exceeds 60 days is considered a storage vessel. A storage vessel does not include (1) a vessel that is skid-mounted or permanently attached to a mobile source and located at the site for less than 180 consecutive days, such as a truck or railcar, (2) a process vessel such as a surge control vessel, bottom receiver, or knockout vessel, or (3) a pressure vessel designed to operate in excess of 204.9 kilopascals without emissions to the atmosphere.
Reason for Request
Ease of understanding

## Slide 2
Appendix A: Direct Testimony of Il Kim

## Slide 3: Commercial Disposal Group: Storage Vessels, Section 123.A
Proposed Language
20.2.50.123.A. Applicability:
(1) [No changes to NMED’s paragraph]
(2) Storage vessels are not subject to Section 123.B. where the use of air pollution control technology would be technically infeasible for reasons including but not limited to the inability to operate without supplemental fuel. The Department can request information at any time regarding the owner’s or operator’s infeasibility calculation. OR (2) Storage vessels for which vapors do not meet minimum Btu values for the combustion device based on manufacturer specifications, are not subject to Section 123.B.
Reason for Request
Oil collected from water operations is less volatile and is considered “dead” oil
Any benefit of controlling low-emitting storage vessels is diminished by the need to import supplemental fuel and burn pilot gas 24/7
E&P facilities generally can route emissions to other tanks or existing controls, while water facilities must retrofit facilities to accommodate combustors